## Slide 1
FILTER
ARRAY
DFE
By:
Mustafa Tamer Mansour EL-Sherif
Amira Atef Ismaeil EL-Komy
Omar Ayoub

## Slide 2
AGENDA
OUR
  PROJECT OVERVIEW
  SYSTEM ARCHIECTURE
  FPGA & FILTER INTEGERATION
  TESTING AND VERIFICATION
  RESULTS AND CONCLUSION

## Slide 3
OVERVIEW
PROJECT
  FRACTIONAL POLYPHASE DECIMATOR (9 MHZ → 6 MHZ)
  Dual 2nd-order IIR notch filters (2.4 MHz, 5.0 MHz)
  Configurable CIC decimator (D = 2, 4, 8, 16)
  Control, status, and debug/probe registers

## Slide 4
ARCHITECTURE
SYSTEM
  HIGH LEVEL DESIGN AND MODELING

## Slide 5
POLYPHASE
FRACTIONAL DECIMATOR
  Passband ripple: ~0.2145 dB
  Stop-band attenuation: ~81.754 dB
  Narrow transition band: 2.8 - 3.2 MHz

## Slide 6
POLYPHASE
FRACTIONAL DECIMATOR

## Slide 7
IIR
  Notch depth: ~ -60.61 dB
  BW: 50 KHz

## Slide 8
IIR

## Slide 9
CIC
  Number of Stages: 1
  Differential Delay: 1
  R: {2, 4, 8, 16}

## Slide 10
CIC

## Slide 11
APB INTERFACE
  Monitoring
  Configuration

## Slide 12
ARITHEMATICS
  Product (Width / Fraction): DATA + COEFF
  Accumulator Width: Product Width + clog2(gain)
  Accumulator & Product: Same fraction length

## Slide 13
TOOLING
PYTHON
  Implements full DFE chain: Fractional Decimator → 2.4 MHz Notch → 5 MHz Notch → CIC
  Supports fixed-point and floating-point processing (s16.15 for fixed)
  Configurable via binary cfg.txt (bypass modes, CIC decimation factor)
  Generates multiple test cases with interference, tones, and noise
  Supports full-flow mode (decimation factors 2/4/8/16) and all bypass combinations
  Writes per-stage outputs for testbench and MATLAB verification

## Slide 14
& TESTING
CONFIGURATION
Test Case | Frequency | Amplitude | Shape | Interference | Tones | Noise
TC_1 | 100 KHz | 0.125 | Sine | ✘ | ✘ | ✘
TC_2 | 100 KHz | 0.125 | Sine | ✔ | ✘ | ✘
TC_3 | 100 KHz | 0.125 | Sine | ✔ | ✔ | ✘
TC_4 | 100 KHz | 0.125 | Sine | ✘ | ✘ | ✔
TC_5 | 100 KHz | 0.125 | Sine | ✔ | ✘ | ✔
TC_6 | 100 KHz | 0.125 | Sine | ✔ | ✔ | ✔

## Slide 15
& TESTING
CONFIGURATION
Test Case | Frequency | Amplitude | Shape | Interference | Tones | Noise
TC_7 | 100 KHz | 0.9999 | Sine | ✘ | ✘ | ✘
TC_8 | 100 KHz | 0.9999 | Sine | ✔ | ✘ | ✘
TC_9 | 100 KHz | 0.9999 | Sine | ✔ | ✔ | ✘
TC_10 | 100 KHz | 0.9999 | Sine | ✘ | ✘ | ✔
TC_11 | 100 KHz | 0.9999 | Sine | ✔ | ✘ | ✔
TC_12 | 100 KHz | 0.9999 | Sine | ✔ | ✔ | ✔

## Slide 16
& TESTING
CONFIGURATION
Test Case | Frequency | Amplitude | Shape | Interference | Tones | Noise
TC_13 | 50 KHz | 0.125 | Sine | ✔ | ✘ | ✔
TC_14 | 200 KHz | 0.125 | Sine | ✔ | ✘ | ✔
TC_15 | 50 KHz | 0.9999 | Sine | ✔ | ✘ | ✘
TC_16 | 200 KHz | 0.9999 | Sine | ✔ | ✘ | ✘

## Slide 17
RESULTS
VERIFICATION
Fixed Point Sample

## Slide 18
RESULTS
VERIFICATION
Floating Point

## Slide 19
RESULTS
VERIFICATION
Max default amplitude error: 0.000248167
Max Error throughout simulations: 6.62038
Floating Point

## Slide 20
RESULTS
VERIFICATION
Status Behavior

## Slide 21
RESULTS
VERIFICATION
APB Point: COEFF.

## Slide 22
RESULTS
VERIFICATION
APB Point : COEFF.

## Slide 23
RESULTS
VERIFICATION
APB Point : COEFF. Behavior

## Slide 24
RESULTS
VERIFICATION
APB Point : COEFF. Behavior

## Slide 25
RESULTS
VERIFICATION
APB Point : COEFF.

## Slide 26
RESULTS
VERIFICATION
Total Latency 1.2µsec

## Slide 27
INTEGERATION
MATLAB
  Filter Modeling
  Filter Analysis
  SIR Calculations

## Slide 28
INTEGERATION
MATLAB

## Slide 29
  Utility
INTEGERATION
FPGA
  HOW IS IT IMPLEMENTED AND TESTED?
Xc7a200t – Artix-7 FPGA

## Slide 30
  Timing
INTEGERATION
FPGA
  HOW IS IT IMPLEMENTED AND TESTED?

## Slide 31
INTEGERATION
FPGA
  HOW IS IT IMPLEMENTED AND TESTED?
  Linting

## Slide 32
INTEGERATION
FPGA
  HOW IS IT IMPLEMENTED AND TESTED?
  Resulted Schematic

## Slide 33
& LIMITATIONS
CHALLENGES

## Slide 34
QUESTIONS?

## Slide 35
YOU
THANK
  VIEW FULL PROJECT ON :
https://github.com/Mustafa11005/Multi_Stage_DFE.git